## Slide 1
Venue/Event
(Sports Game)
Sounds, Lights, CO2, Heat
Data
Camera
Mic
CO2 Sensor
Temperature Sensor
Input Devices
…
Screens
Lights
Confetti
Publish
Subscribe
Gateway
Microcontroller + SigFox
Single board PC + Wi-FI
Linux Box + 4G
PC + 3G
…
Azure Cloud
Publish
Publish
Virtual Machine
Raw Outputs
Cognitive Services
Pub/Sub
SQL DB
Pub/Sub
Open Experience API
Emotion API
Sound API
Attention API
Rowdiness API
Sports Game
Subscribe
Publish
Concert
Publish
Screens
Lights
Sound
In Home Experience
Publish
Subscribe
In Home Events

## Slide 2
HD Camera
Bus
Laptop Running Mac OS
Local HTML 5 Web Application takes a photo every 5 seconds and converts the image as a base64 encoded URI
Local Node.JS app converts the encoded URI to an octet stream
Microsoft Cognitive Services
MS Emotion Recognition API receives the data and detects every emotion for every face
API call to a Node.JS app endpoint with the encoded URL
Sorts and creates SQL statements for every user from JSON object
REST POST call to MS Emotion Recognition API with binary data of image
Returns a response to with JSON object with every face, bounding rectangle, and emotions
Microsoft Azure SQL DB
This table has all the incoming emotion data
Eddystone Beacon with a URL
Dynamic HTML website that uses JSON to fill in content
Microsoft Azure SQL DB
This table has all emotions mapped to some message
Hits the Emotion API every n seconds to get the latest emotion and pull in the message associate with it
Phone
Physical Web – Bluetooth broadcasting URL to all nearby phones with physical capabilities
1
2
3
4
5
6
7
8
9
Makes SQL queries app
10
11
Measuring and responding to emotion in venues in real time using Microsoft Cognitive Services and Azure (Demo)
Emotion API